Pilot Operating Handbook and Airplane Flight Manual

GENERAL

Section I

Table of Contents

IMPORTANT NOTICE

USE OF THIS HANDBOOK
REVISING THIS HANDBOOK
SUPPLEMENTS REVISION RECORD
GROUND TURNING CLEARANCE
THREE VIEW
DESCRIPTIVE DATA
Engines
Propeller
Fuels
Oil Capacities
Weights
Cabin and Entry Dimensions
Baggage
Specific Loadings (Max Take-Off Weioght)

GENERAL AIRSPEED TERMINOLOGY/SYMBOLS
Meterological
Power
Engine Controls/Instruments
Performance and Flight Planning
Weight and Balance
NOTES

THANK YOU.....

You have obtained what we feel is the latest state-of-the-art in the most user(and family)friendly homebuilt aircraft in the world. Its performance is spectacular and its life almost beyond measure given reasonable care. We encourage you to become familiar with this handbook as well as the FARs that are applicable to your operation. The combination will provide you with safe and sound knowledge for operation of your personally manufactured EXPRESS.

IMPORTANT NOTICE
This handbook must be read carefully by the owner or operator(s) of the EXPRESS in order to become familiar with its operation and to obtain all it has to offer in terms of both speed and reliability. Herein are suggestions and recommendations to help you obtain safe performance without sacrificing outstanding economy. You are encouraged to operate your machine in accordance with and within the limits identified in this Pilot's Operating Handbook and Approved Flight Manual as well as any placards located in the airplane.

Again, another reminder- the operator should also be familiar with the Federal Aviation Regulations as applicable to the iperation and maintenance of experimental airplanes and FAR Part 91 General Operating and Flight Rules. The aircraft MUST be operated and maintained in accordance with any FAA Airworthiness Directives which may be issued against it. It is also prudent and mandatory to operate within any established limits or Service Bulletins.

The FARs place the responsibility for the maintenance of this airplane on the owner and the operator who must ensure that all maintenance is accomplished by the owner or qualified mechanics in conformity with all airworthiness requirements wstablished for this airplane.

All limits, procedures, safety practices, time limits, servicing, and maintenance requirements contained in this handbook are considered mandatory for the continued airworthiness of this airplane, in a condition equal to that of its original manufacture.

USE OF THIS HANDBOOK

The Pilot's Operating Handbook is designed so that necessary documents may be maintained therein for the safe and efficient operation of your 4-place EXPRESS. It’s loose leaf form allows easy maintenance of updates and revisions, and is also a convenient size for storage and use within the cockpit.

The handbook is in ten basic sections in accordance with the GAMA Specification No.1, Issued 15 February 1975, Revised ! September 1984, Revision #1.

NOTE
Except as noted, all airspeeds quoted in this handbook are Indicated Airspeeds (IAS) in Knots, and assume zero instrument error.

REVISING THIS HANDBOOK
Immediately following the title page is the "Log Of Revisions"page(s). The Log of Revision pages are used for maintaining a listing of all effective pages in the handbook (except the SUPPLEMENTS section). and as a record of revisions to these pages. In the lower right corner of the outlined portion of the Log is a box containing a capital letter which denotes the issue or reissue of the handbook. This letter may be suffixed by a number which indicates the numerical revision. When a revision to any information in the handbook is made, a new Log of Revisions will be issued. All Logs of Revisions must be retained in the handbook to provide a current record of material status until a reissue is made.

WARNING
When this handbook is used for airplane operational purposes,
it is the pilot's responsibility to maintain it in current status.

AIRPLANE FLIGHT MANUAL
SUPPLEMENTS REVISION RECORD
Section IX contains the Express Design Inc. Approved Airplane Flight Manual Supplements headed by a Log of Supplements page. On the "Log" page is a listing of the EXPRESS Approved Supplemental Equipment available for installation on the airplane. When new supplements are received or existing supplements are revised, a new "Log" page will replace the previous one, since it contains a listing of all previous approvals, plus the new approval. The supplemental material will be added to the grouping in accordance with the descriptive listing.
NOTE

Upon receipt of a new or revised supplement, compare the "Log of Revisions" page just received with the existing Log page in the manual. Retain only the new page with the latest date on the bottom of the page and discard the old one.

DESCRIPTIVE DATA

ENGINE	Lycoming, IO-360 C1C6

PROPELLER	Hartzell, 2 Blade 7666A-2, HCE2YR Hub

FUEL	100LL (blue) Av gas

Standard System Capacities
Main, Useable	46.0 gallons (U.S.)
Auxiliary wing tanks	34.0 gallons

OIL CAPACITY

8 quarts (U.S.)

WEIGHTS

Max Take-off Weight	2895 lbs.
Max Landing Weight	2895 lbs.
Max Baggage Comp.(4 per, full fuel) (per Wt & bal) lbs.

CABIN AND ENTRY DIMENSIONS

Height	44.5 inches

Width - Interior, front	45 inches

Width - Interior, rear	42.75 inches

BAGGAGE

Compartment Volume	20.6 cu ft

SPECIFIC LOADINGS (Max Take-off Wt.)

Wing Loading - 200HP	21.1 lbs/sq ft
Power Loading - 200HP	14.5/lbs/hp
Useful Load - 200 HP	1195 lbs

GENERAL AIRSPEED TERMINOLOGY AND SYMBOLS

CAS	Calibrated Airspeed is the indicated speed of an	airplane, corrected for "position error" and instrument error.	Calibrated airspeed is equal to true airspeed
in standard atmosphere at sea level.

GS	Ground Speed is the speed of an airplane relative to the ground.

IAS	Indicated Air Speed is the speed of an airplane as shown on the airspeed indicator when corrected for instrument error. IAS values published in this hand-book assume zero instrument error.

KCAS	Calibrated Airspeed expressed in "knots."

KIAS	Indicated Airspeed expressed in "knots."

TAS	True Airspeed is the airspeed of an airplane relative	to undisturbed air which is the CAS corrected for altitude, temperature, and compressibility.

VA	Maneuvering Speed is the maximum speed at which	application full	available aerodynamic control will not	overstress the airplane.

VFE	Maximum Flap Extend Speed is the highest speed	permissible with wing flaps in a prescribed extended position.

VNE	Never Exceed Speed is the speed limit that may not be exceeded at any time.

VNO	Maximum Structural Cruising Speed is the speed that should not be exceeded except in smooth air and then	only with caution.

VS0	Stalling Speed or the minimum steady flight speed at which the airplane is controllable in the landing configuration.

VS1	Stalling Speed or the minimum steady flight speed at which the airplane is controllable

VX	Best Angle-of -Climb Speed is the airspeed which	delivers the greates gain of altitude in the shortest possible	horizontal distance. Also, speed for rotation on takeoff.

VY	Best Rate-of -Climb Speed is the airspeed which	delivers the greates gain in altitude in the shortest possible	time.

METEOROLOGICAL TERMINOLOGY

ISA	International Standard Atmosphere in which
1) The air is a dry perfect gas;
2) The temperature at sea level is 15 Celsius (59 F);
3) The pressure at sea level is 29.92 in. Hg. (1013.2 mB);
4) The temperature gradient from sea level to the altitude at	which the outside air temperature is -56.5C (-69.7F) is - 0.	00198C (-0.003566F) per foot and zero above that altitude.

OAT	(Outside Air Temperature) The free air static temperature,	obtained either from in-flight temperature indicators adjusted	for instrument error and compressibility effects, or ground	meteorological sources.

Indicated Pressure Altitude	The number actually read from an altimeter when the barometric subscale has been set to	29.92 in Hg or 1013.2 millibars.

Pressure Altitude	Altitude measured from standard sea-level pressure (29.92 in Hg) by a pressure or barometric altimeter. It is the indicated pressure altitude corrected for position and instrument error. In this handbook, altimeter instrument errors are assumed to be zero. Position errors may be obtained from the Altimeter Correction Graph.

Staion Pressure	Actual atmospheric pressure at field	elevation.

Wind	The wind velocities recorded as variables on the charts of	this handbook are to be understood as th headwind or	tailwind components of the reported winds.

POWER TERMINOLOGY

Take-off and Maximum Continuous	The highest power rating not	limited by time.

Cruise Climb	The power recommended for cruise climb.

ENGINE CONTROLS/INSTRUMENTS

Throttle Control	Used to control power by introducing fuel-air	mixture into the intake passages of the engine. Settings are	reflected by readings on the manifold pressure gauge.

Propeller Control	This control requests the propeller to	maintain engine/propeller rpm at a selected value by	controlling blade angle.

Mixture Control	This control is used to set fuel flow in all	modes of operation and cuts off fuel completely for engine	shutdown.

EGT (Exhaust Gas Temperature)	This indicator is used to	identify the lean and best power fuel flow for various power	settings.

CHT (Cylinder Head Temperature)	This indicator is used to	identify the operating temperature of the engine’s cylinders.

Tachometer	Indicates the RPM of the engine/propeller.

Propeller Governor	Regulates the RPM of the engine/propeller	by increasing or decreasing the propeller pitch change	mechanism in the propeller hub.

AIRPLANE PERFORMANCE AND FLIGHT PLANNING TERMINOLOGY

Climb Gradient	The ratio of the change in height during a	portion of a climb, to the horizontal distance traversed in the	same time interval.

Demonstrated Crosswind Velocity	The velocity of the crosswind	component for which adequate control of the airplane duriong	take-off and landing was actually demonstrated. The value	shown is considered to be limiting.

MEA	Minimum enroute IFR altitude.

Route Segment	A part of a route. Each end of that part is	identified by:
1) a geographic location
2) a point at which a definite radio fix can be	established.

GPH	Gallons per hour fuel flow.

PPH	Pounds per hour fuel flow

WEIGHT AND BALANCE TERMINOLOGY

Reference Datum	An imaginary vertical plane from which all	horizontal distances are measured for balance purposes.

Station	A location along the airplane fuselage usually given	in terms of distance from the reference datum

Arm	The horizontal distance from the reference datum to	the center of gravity (CG) of an item.

Moment	The product of the weight of an item multiplied by its	arm. (Moment divided by a constant may be used to simplify	balance calculations by reducing the number of digits.

Airplane Center of Gravity (CG)	The point at which an	airplane would balance if suspended. Its distance from the	reference datum is found by dividing the total moment by the	total weight of the airplane.

CG Arm	The arm obtained by adding the airplane’s individual	moments and dividing the sum by the total weight.

CG Limits	The extreme center of gravity locations within which	the airplane must be operated at a given weight.

Useable Fuel	The fuel available for flight planning purposes.

Unuseable Fuel	Fuel remaining after a runout test has been	completed in accordance with government regulations.

Standard Empty Weight	Weigth of a standard airplane including unuseable fuel, full operating fluids and oil.

Basic Empty Weight	Standard empty weight plus any	optional equipment.

Payload	Weight of occupants, cargo, and baggage.

Usefull Load	Difference between take-off weight, or ramp weight if	applicable, and basic empty weight

Maximum Ramp Weight	Maximum weight approved for	ground maneuvering. (It includes the weigth of start, run-up,	and and taxi fuel)

Maximum Take-off Weight	Maximum weight approved for the	start of the take-off run.

Maximum Landing weight	Maximum weigth approved for the	landing touchdown.

Zero Fuel Weight	Weight exclusive of useable fuel.

Tare	The weights of chocks, blocks, stands, etc.used on the scales	when weighing an airplane.

Jack Points	Points on the airplane identified by the manufacturer	as suitable for supporting the airplane for weighing or other	purposes.

Limitations

Section II
Table of Contents

GENERAL
AIRCRAFT OPERATING SPEEDS
POWERPLANT LIMITATIONS
OPERATING LIMITATIONS - 200 HP IO-360C1C6
OIL SPECIFICATION
PROPELLER
POWERPLANT INSTRUMENT MARKINGS
INSTRUMENT MARKINGS
WEIGHT LIMITS
CENTER OF GRAVITY LIMITS
REFERENCE DATUM
MANEUVERING LIMITS
DEMONSTRATED MANEUVERS
FLIGHT LOAD FACTOR LIMITS
TYPES OF OPERATION AND LIMITS
FUEL QUANTITIES
WINTER OPERATIONS
PLACARDS
KINDS OF OPERATIONS
MINIMUM EQUIPMENT LIST (MEL)
NOTES

GENERAL

The data approved by Express Design Inc. (EDI) and the Limitations presented herin are those established by EDI as applicable to the Express aircraft.

This section follows the format approved by the GAMA Specification #1, and is intended to provide operating guidelines and limitations specific to the Express aircraft only. All airspeeds quoted are given conventional nomenclature, are shown in knots, calibrated airspeed, and assume zero instrument error.

AIRCRAFT OPERATING SPEEDS

Express Aircraft, General

SPEED	MARKINGS	KCAS	(mph)
Never Exceed Speed	Vne	Red Line	204	(235)
Caution, smooth air only	Yellow Arc	123-151 (142-174)
Maneuvering Speed	Va	123	(142)
Normal Op Range	Vno	Green Arc	104-151 (120-174)
Full Flap Op Range	Vfe	White Arc	50-87	(58-100)
Clean Stall Speed	Vs	55	(63)
Stall Speed Ldg Config	Vso	50	(58)

POWERPLANT LIMITATIONS
OPERATING LIMITATIONS

200 HP, IO360C1C6 (LYCOMING SPECIFICATION)

T.O. & Max Continuous RPM
Full Throttle, red line	2700 RPM
Normal Operation	600 (idle) 2350 - 2450 rpm (cruise)

Cylinder Head Temperatures
Maximum	475F (246C)
Normal Operating Range	325 - 380F (163 - 193C)
Recommended	150 - 435F (65-223C)

Oil Temperatures
Maximum	240F (115C)
Desired Operating	160 - 180F (71 - 82C)

Oil Pressure
Minimum Operating (idle)	10 psig
Normal Operation	30 - 60 psi
Maximum (starting & warm up)	100 psi

Fuel Flow
Cruise	65% = 61#/hr, 75% = 79#/hr

Fuel Pump Inlet Pressure
Maximum	+8.0 psig (0.54 atm)
Recommended	-1.0 psig (-0.07 atm)
Minimum	-2.0 psig (-0.14 atm)

Vacuum Pressure
Normal Operating Range	4.3 - 5.9 In. Hg

Fuel Grade	100 LL
Maximum Lead content	2 cc/gal

OIL SPECIFICATION

Following initial break-in of the engine it should be operated with an ashless dispesant oil (MIL-L-22851) conforming to the applicable Lycoming engine handbook. Break-in (the first 50 hours or until oil consumption has been stabilized) should be accomplished using a corosion preventative oil or straight mineral oil. Low power settings (less than 65-75%) should be avoided during the break-in period and the oil level checked frequently.

POWERPLANT INSTRUMENT MARKINGS

It is recommended that the following markings be made on the engine instrument gauges to conform to convention.

OIL TEMPERATURE
Caution (Yellow Radial)	200 - 240F
Normal Oper. Range (Green Arc) 160 (170) to 180 (220) F	Maximum (Red radial)	240F

OIL PRESSURE
Minimum (Idle, Red radial)	10 psi
Caution Range (Yellow arc)	10 - 30 psi
Operating Range (Green arc)	30 - 60 psi
Maximum - Cold oil (Red radial)	100 psi

TACHOMETER
Operating Range (Green arc)	600 to 2750 (2450) rpm
Maximum (Red radial)	2800 (2500) rpm

CYLINDER HEAD TEMPERATURE
Operating Range (Green arc)	240 to 380F
Maximum (Red radial)	460F
Recommended T.O.	240F

MANIFOLD PRESSURE

Operating range (Green arc)	15 to 29.6 in. Hg.
Maximum (red radial)	29.6 in. Hg.

FUEL FLOW - Lbs/Hr.
Operating Range (Green arc)	45% (85%)
41 to 77 (53 to 113)
Maximum Flow	(Red radial)	110 (130)

VACUUM PRESSURE
Operating Range (Green arc)	4.3 to 5.9 in. Hg.

WEIGHT LIMITS, Express FG - 200 HP:
Maximum Ramp, T.O. & Landing Weight	2895 lbs.
Maximum Baggage Weight	250 lbs.

CENTER OF GRAVITY LIMITS

FORWARD LIMITS

The allowable Center of Gravity (CG) range is from Fuselage Station (FS) 74 to FS 84.95.

AFT LIMIT

The aft CG limit is FS 84.95 inches, and must be considered a firm limit. Loadings which place the CG further aft are dangerous and must not be accepted. A “Weight and Balance” sheet must be completed and carried in the aircraft at all times. See section VI.

REFERENCE DATUM

A Fuselage Station (FS) datum must be used to establish the aircraft weight and balance. FS 34, the forward face of the firewall, is generally a convenient location regardless of engine configuration.

MANEUVERING LIMITS

The Express Model FG is licensed as EXPERIMENAL. Spins are not approved. Maneuvers which have been flown by Express Design approved test pilots are shown in the chart below. Care must be used and smooth control inputs used at all times when performing maneuvers which involve unusual aircraft attitudes, and instruction in such maneuvers is considered prudent.

DEMONSTRATED MANEUVERS

MANEUVER	ENTRY SPEED	MAX G’S
Chandelle	160 Kts.	3.5
Lazy Eight	189 Kts.	1.0 to 1.5
Stalls (not whip stalls)	0.0 to 1.5

WARNING

Since the IO 360C1C6 engine does not have an inverted oil system extreme care must be used during low or negative G maneuvers. Lack of oil pressure may cause the propeller to go to flat pitch and engine overspeed will result. Transient oil pressure conditions near zero must be limited to less than two seconds.

NOTE

All pilots are again reminded that instruction in unusual attitudes in the Express is highly desireable. Speed buildup during maneuvers can be rapid and proper control useage throughout the maneuver to remain within limits.

Minimum fuel in the tank under use is 20 gallons, auxilliary wing tanks should be empty. Sideslips should be limited to 30 seconds maximum and oil pressure should be monitored in accordance with the note above and fuel should be selected from the high wing during sideslips.

FLIGHT LOAD FACTOR LIMITS
Flaps up	+4.5 to -2.3 g’s
Flaps down	+2.5 to -2.0 g’s
Design Ultimate (Flaps up)	+8.8 to -4.4 g’s

MINIMUM FLIGHT CREW

Minumum crew is one (1) pilot

TYPES OF OPERATIONS AND LIMITS

The Express Model FG approved for the following types of flight when the required equipment is installed and operations are conducted as defined in this LIMITATIONS section.

1. VFR, day and night
2. IFR, day and night

WARNINGS
1. Flight operations with passengers for hire and
2. Flight into known icing is prohibited.

FUEL QUANTITIES
Standard Wing Tank (23 gal eachwing) 46 gallons useable
Extended Wing Tank (17 gal each wing) 34 gallons useable
Total	80 gallons

FUEL MANAGEMENT

Do not take off with less than 8 gallons in the wing tanks. Fuel must be used from each wing by the pilot, maintainig left/right wing balance, KNOW YOUR SYSTEM! Many accidents involve fuel, - lack of fuel or mishandling of onboard fuel.

SEATING

This aircraft seats four adults, side by side,two front and two rear, and can be flown from either front seat. The aft seats can be be both forward or the left rear facing aft for imroved rear passenger conversations.

WINTER OPERATIONS

Winter operations are acceptable with proper oil grades for the operatng temperature.

PLACARDS

All switches, lights, controls, adjustments and circuit breakers etc. should be marked with labels identifying what the switch, control, etc. is related to and what the position selects.

Safety related items such as door opening instructions, emergency shut-offs, and seat belt/shoulder harness requirements should be placed where obvious and made clearly understandable. An example of this would be the door openning procedure. It should be placed approximately near the door handle as well as being available in the EMERGENCY Section of this handbook (Red Tab).

An example of a switch marking is the strobe light switch. It should be labeled as “Strobe” with “on” and “off’ positions identified. Convention is up is “on” and down is “off” for electrical switches. Circuit breakers should be labeled as to their rating, i.e. “5 amp”, “3 amp”. etc.

NOTE
There are two placards that must be installed.

1. The word “EXPERIMENTAL” must be placed where it can be prominently seen upon entry into the cabin. These letters must be at least three inches high, and contrast sufficiently to be seen on entry.

2. The baggage compartment must have a placard showing the maximum baggage allowed as shown on the weigth and balance data sheet for the airplane.

In addition, the following are some recommended placards:

In front of the pilot:

Airspeed Limitations
Max Flap extend speed 98 kts
Max Full Flaps 98 kts

Near the main wing tank gauges:

Do Not Take Off With Less Than
12 Gallons in Main Tanks

Near the extended range tank fuel gauges:

 17 Gallons 17 Gallons
useable useable

If strobe equiped:

Turn Strobe OFF when taxiing in vicinity of other
aircraft or when flying in fog/clouds. Standard
position lights to be used for all night flights

Near canopy latch:

Latch Door Before Takeoff
DO NOT OPEN IN FLIGHT

Special precautions should e used during flights in/around areas of atmospheric electrical activity as in thunderstorms. This aircraft, being of composite construction, conducts electricity most readily thu such as control cables, wiring, etc., a condition to AVOID.

KINDS OF OPERATIONS

EQUIPMENT LIST

This airplane may be operated in day or night VFR or day and night IFR in the United States if the appropriate equipment is installed and operable.
You as the owner are responsible for the make-up of the Minimum Equipment List (MEL) for the airplane, and maintenance thereof prior to operation where the equipment is required. For example for a day flight, the position lights need not be operable, however a strobe or anti-collision light must be.
Minimum Equipment List

  System	VFR, Day

   and/or	VFR, Night

Component	IFR, Day

IFR, Night Remarks

ELECTRICAL POWER
Alternator	0	1	1	1	Desireable
Battery	1	1	1	1	Desireable
Ammeter	1	1	1	1
Voltmeter	0	0	0	0

ENGINE
Cyl Head Temp	0	0	0	0	Desireable
Exhaust Gas Temp	0	0	0	0	Desireable
Manifold Pressure	1	1	1	1
Oil Pressure	1	1	1	1
Oil Temperature	1	1	1	1

FLIGHT CONTROLS
Elevator Trim System	1	1	1	1
Flap Position Indicator	0	0	0	0	Desireable

FLIGHT INSTRUMENTS
Airspeed Indicator	1	1	1	1
Altimeter	1	1	1	1
Magnetic Compass	1	1	1	1
Outside Air Temp.	0	0	0	0	Desireable

FUEL SYSTEM
Fuel Quantity Gauges	1	1	1	1
Fuel Boost Pump	1	1	1	1	Desireable
Fuel Selector Valve	1	1	1	1
  System	VFR, Day

   and/or	VFR, Night

Component	IFR, Day

IFR, Night Remarks

ICE/RAIN EQUIP.
Pitot Heat	0	0	0	0	Desireable

LIGHTS
Cockpit Lights	0	1	0	1	Desireable
Landing Lights	0	0	0	0	Desireable
Nav. (Posn) Lights	0	3	0	3
Rotating Beacon/Strobe	0	1	0	1

PNEUMATIC SYSTEM
Instrument Vacuum	0	1	1	1
Pressure Gauge	0	1	1	1

PUBLICATIONS
Pilots Oper. Hndbk. &
 Airplane Flight Manual	1	1	1	1
Weight and Balance	1	1	1	1
Pilots License/Medical	1	1	1	1
Radio License	1	1	1	1
Airworthiness Cert.	1	1	1	1
Registration	1	1	1	1
Maps, VFR flight	1	1	1	1	Desireable
Charts/Appr. Plates	0	0	1	1

RESTRAINT SYSTEM
Seat Belt/Occupant	1	1	1	1
Shoulder Harness	0	0	0	0	Desireable
Baggage Tiedown	0	0	0	0	Desireable

Emergency
Procedures

Section III
Table of Contents

EMERGENCY AIRSPEEDS
ENGINE FAILURE
Rough Running Engine
ENGINE FIRE
In Flight
On Ground
EMERGENCY DESCENT
MAXIMUM GLIDE CONFIGURATION
LANDING EMERGENCIES
LANDING WITHOUT POWER
SYSTEM EMERGENCIES
Propeller Overspeed
Propeller Damage
Electrical System Failure
Landing Gear
Unlatched Door In Flight
SPINS
EMERGENCY SPEED REDUCTION
NOTES

NOTE:
All airspeeds quoted in this section are indicated airspeeds (IAS) and assume zero instrument error. The aircraft should be calibrated to determine its specific error for various configurations.

EMERGENCY AIRSPEEDS

ITEM	CONDITION
Emergency Descent	153 kts

Best Glide	90 kts (103 mph)

Landing Approach (w/o power)	80 kts (92 mph)

NOTE:
The following check-lists are presented to capture in a compact format those pilot tasks requiring rapid action. These check-lists should be kept handy for ready access by the pilot, and he should familiarize him/herself with them before flying the aircraft. Knowledge of the switch, control, gauge, etc. location quickly, even blindfolded, is highly desireable.

ENGINE FAILURE

Take-off Ground Roll/Low Altitude (Less than 700’ AGL)
Maintain control of the aircraft. If runway permits, land and attempt to stop on runway. If at low altitudes, (less than approximately 700’ AGL), pick the most suitable site within +/- 30 off the nose and set up the approach. If time permits, attempt engine start.

ITEM	CONDITION

Establish	90 kts
Declare	Emergency
Check Fuel Boost Pump	ON
Mixture	Rich
Magnetos, cycle & return to	Both
Flaps on final	Full

In Flight
Establish 90 kt glide. Climb to reduce speed if practical, pick landing site. Attempt AIR START.

ITEM	CONDITION

Check main tank for fuel	Select tank if req’d.
Fuel boost pump	ON emergencies
Mixture	RICH
Cycle mags & return to	BOTH
Engage starter and attempt engine start
Declare	EMERGENCY
Give posn. on freq or	121.5
Set transponder to	7700

NOTE
If power is restored and there is any doubt as to the cause of the engine stoppage, land at the nearest airpot and determine the cause.

ROUGH RUNNING ENGINE

 ITEM	CONDITION
Adjust Mixture	RICH
If no improvement carefully lean for improvement as follows:

ITEM	CONDITION
Pwr setting to approx.	2100 rpm (see Eng. Manual)
Mags, Sw to LT, BOTH, RT, then to	BEST
Readjust mixture for	best operation

NOTE
If power is restored and there is any doubt as to the cause of the engine roughness, land at the nearest airpot and determine the cause.

ENGINE FIRE

IN FLIGHT
Determine if fire is electrical (Acrid smell)
ITEM	CONDITION
Avionics Master	OFF
Master Switch	OFF
All Radios, lights, etc.	OFF

If fire/smell clears, turn master switch ON then each item of	equipment one at a time, waiting long enough to isolate	cause. If no smell, assume an unknown source and:
Land as soon as possible, find and correct cause.

If fire continues:
ITEM	CONDITION
Throttle	IDLE
Mixture	CUT-OFF
Fuel Shut-Off Valve	OFF
Fuel Boost Pump	OFF
Transponder	7700
Radio	Emergency & Location
(Use active frequency or 121.5)

Land immediately and exit the aircraft.

On ground (engine start or taxi)
ITEM	CONDITION
Throttle to	IDLE
Mixture	CUT-OFF
Radio (Twr, Unicom, etc.)	EMERGENCY &
POSITION
Master Switch	OFF

Continue cranking if during start to pull fire back into the engine. Stop and exit aircraft if taxiing. If unable to stop fire by above means, loose dirt, sand, may be used thru cooling intakes to quench fire if no extinguisher is available.

EMERGENCY DESCENT

ITEM	CONDITION
Power to	IDLE
Propeller to	HIGH RPM
Maintain	153 kts (176 mph)
Transponder	7700 or as requested

MAXIMUM GLIDE CONFIGURATION

ITEM	CONDITION
Establish	90 kts (103 mph)
Flaps	UP
Propeller	LOW RPM

Glide distance is approximately 1.3 nm (1.5 statute miles) per 1000 feet of altitude above terain, however this may vary significantly.

LANDING EMERGENCIES

Landing without power
When landing site is selected and committed to landing the following checklist can be completed. If the terrain is harsh the gear may well absorb energy and although resulting in substancial damage to the aircraft may, in that process, afford some protection to the occupants and thereby a desireable result. When assured of reaching the landing area or committed:

ITEM	CONDITION
Seat Belts/Shoulder Harness	TIGHT
Door	LATCHED
Fuel Boost Pump	OFF
Mixture	CUT-OFF
Mags	OFF
Flaps	AS REQUIRED
Master	OFF
Airspeed	Decrease to Toughdown

Attempt to fly the aircraft and keep the wings level through the approach and landing until the aircraft comes to a complete rest. EXIT THE AIRCRAFT and remain clear until assured there is no possibility of fire.

SYSTEMS EMERGENCIES

PROPELLER OVERSPEED
The controllable pitch propeller with governor used on the Express
utilizes oil pressure from the governor to increase pitch (low rpm).

It is however dangerous to run any engine over its rated rpm and thus the method to reduce any overspeed is to immediately reduce the throttle to idle and reduce airspeed to the point where rpm control is regained. Slowly add throttle and hold airspeed well below that at which the overspeed occured. Mixture may need to be adjusted also for smooth operation. If the overspeed was significant, i.e. over 200rpm over redline, an engine inspection is called for upon landing. Engine operation for the balance of the flight ust be monitored closely.

PROPELLER DAMAGE
The propeller needs proper care. Nicks, scratches, and other types of damage require care. While the construction varies, all are highly stressed and nicks can cause stress concentrations that can result in catastrophic failures of the propeller. Refer to the manual for the propeller for proper limits of acceptable damage.

ELECTRICAL SYSTEM FAILURE
The electrical system of this aircraft is key to safe operation in today’s environment. It is required for night or IFR operations. The voltmeter is your key indicator of alternator failure which then places the entire electrical load on the battery. The battery will read approximately 12.4 volts on a full battery, and 14+ on the alternator. If you experience alternator failure:

ITEM	CONDITION
If IFR/IMC	Notify ATC Immediately
Master Switch	OFF
Avionics Master	OFF
Lights	OFF
Circuit Breakers	Check

A check of the Circuit Breakers may reveal a popped breaker indicating the source of the trouble. If so , turn all individual equipment OFF, reset the breaker and turn the Master Switch ON. If the breaker does not trip again after a few minutes , slowly turn various elements of you system ON one at a time watching for another malfunction attempting to isolate the problem.

If you feel you have isolated the problem and elect to continue the flight, remain particularly alert for another malfunction caused by/related to the first.

UNLATCHED COCKPIT DOOR IN FLIGHT
The Express door must not be opened in flight. Should a latch become disengaged, cautiously slow the aircraft to approximately 85 kts (100 mph) and attempt to relock without opening any further and/or have a passenger hold the door closed. If this fails , continue the flight at that speed and land as soon as possible.

SPINS
Intentional spins are not allowed. If a spin is entered inadvertantly, reduce the power to idle, neutralize the stick or place forward long enough to break the stall, and place the rudder full against the direction of the spin until rotation is stopped. At this point the aircraft should be recovered to level flight, with smooth positive load factor (pull-out), wings level, of no more than 4 g’s (4g’s can generally be noticed by a noticeable sagging of your jaw and cheeks) taking particular care not to reenter an accellerated stall (noticeable by sharper, more positive than normal pre-stall buffeting ) and another spin. Should this pullout buffeting occur, simply relax somewhat on the back pressure till bufeting ceases and continue the pullout. If the spin has been allowed to develop, a temporary application of power may aid in recovery

WARNING
The Express aircraft is aerodynamically very clean and thus can cosume a lot of altitude with such maneuvers.

EMERGENCY SPEED/ALTITUDE REDUCTION
Speed reductions should be accomplished by idle power settings and high rpm settings to allow the engine and propeller to assist in the speed reduction. this will cause rapid cooling of the engine but is an acceptable alternative in most cases. This procedure may be appropriate after entry into IMC by a disoriented or non-rated pilot. Even flaps can be extended if necessary, although such a procedure should be followed by an appropriate inspection.

Normal Procedures

Section IV
Table of Contents

SAFE OPERATING AIRSPEEDS
PREFLIGHT INSPECTION
Cockpit - (Checklist)
Walk Around Inspection - (Checklist)
Before Starting - (Checklist)
Starting - (Checklist)
Cold Starting
Flooding Engine - (Checklist)
Hot Strting
Pre-Taxi Checks - (Checklist)
Pre take-Off Run-up - (Checklist)
Before Take-Off - (Checklist)
Runway Checks - (Checklist)
Take-off&Climb - (Checklist)
Cruise - (Checklist)
LEANING, GENERAL
Leaning, Exhaust Gas Temperature
Leaning, Flowmeter
Leaning, Manual Mixture Control
USE OF ALTERNATE AIR
ADDITIONAL CHECKLISTS
Descent - (Checklist)
Pre-Landing - (Checklist)
Balked Landing - (Checklist)
After Landing - (Checklist)
Shutdown - (Checklist)
ABBREVIATED TAKE-OFF CHECKLIST (CIGAR)
ABBREVIATED LANDING CHECKLIST (GUMP)
HEATING AND VENTILATION
COLD WEATHER OPERATIONS
ICING CONDITIONS
NOISE
NOTES

SAFE OPERATING AIRSPEEDS

NOTE
All airspeeds in this section are indicated airspeeds (IAS) and assume zero instrument error. You should make sure your system has been correctly calibrated and account for any errors as necessary.

Max Demonstrated X-WIND Component-	20 kts

Express speeds
1) Take-off, flaps up
    Rotation	65-70kts(75-80mph)
    50 feet	65kts(75mph)

2) Take-off, Flaps APPROACH(1/3)
    Best angle of climb	65kts(75mph)
    Best rate of climb	70kts(80mph)
    Cruise Climb	90-100kts(104-115mph)

3) Landing approach
    Flaps DOWN(1/3)	65kts(75mph)
    Flaps UP (0 deg, faired)	70kts(80mph)

4) Balked Landing Climb	70kts(80mph)
   (on establishment of positive climb)

PREFLIGHT INSPECTION

COCKPIT - (Checklist)

ITEM	CONDITION

1) Control Lock	REMOVE
2) Avionics master switch	OFF
3) Master Switch	ON
4) Fuel Quantity Gauge	CHECK
5) Lights (If night flight)	CHECK
6) Flaps	DOWN
7) Pitot Heat (If IFR/IMC)	CHECK
8) All Switches	OFF

WALK AROUND INSPECTION - (Checklist)
(Starting at right wing/fuselage)

ITEM	CONDITION

1) Right Flap Attach’mt (Lower side)	Secure
2) Right Aileron
    Hinges	Secure
    Motion	Free
    Span Edges	No interference
3) Wing Tip	No damage, light secure
4) Wing Upper/Lower Surface	Sight - smooth
    Inspection Plates	Secure
    Leading Edge	Feel for damage
    Fuel Quantities	Check, Caps secure
    Fuel Drains	Strain, check for water
5) Right Main Gear
    Tire	Check tread, inflation
    Chocks	Removed
    Brake pads	Check
    Brake Line	Condition
    Fairing	Secure
6) Cowling area
    Tire	Check tread, inflation
    Chocks	Removed
    Screws/retainers	Secure
    Cooloing Intakes	Clear
    Oil	Check quantity, door secure
    Spinner	Secure
    Blades	No Damage

WARNING
Always assume the propeller is “Hot” and the engine ready to start when handling the propeller regardless of mag position.

CAUTION
See propeller manufacturer’s instructions for nick and damage treatments and limitations. Damaged propellers are dangerous and can result in catastrophic failures.

8) Left Main Gear
    Tire	Check tread, inflation
    Chocks	Removed
    Brake pads	Check
    Brake Line	Condition
    Fairing	Secure
9) Wing Upper/Lower Surface	Sight - smooth
    Inspection Plates	Secure
    Leading Edge	Feel for damage
    Fuel Quantities	Check, Caps secure
    Fuel Drains	Strain, check for water
10) Wing Tip	No damage, light secure
11) Left Aileron
     Hinges	Secure
     Motion	Free
     Span Edges	No interference
12) Left Flap Attach’mt (Lower side)	Secure
13) Tail Assembly
      Horizontal Stabilizer	No leading edge damage
      Vertical Stabilizer	No leading edge damage
      Elevator/Rudder	Free motion
      Hinges	Secure
      Rudder Cables	Secure

BEFORE STARTING - (Checklist)
1) Baggage	Stowed, loose items SECURED
2) Seat Belts	Adjusted and SECURED
3) Brakes	SET
4) Circuit Breakers	Checked and IN
5) Master Switch	OFF
6) Avionics Master Switch	OFF
7) Avionics Switches	OFF
8) Door	LATCHED

STARTING - (Checklist)
1) Master Switch	ON
2) Fuel Quantity	CHECK
3) Cowl Flaps	OPEN
4) Mixture	FULL RICH
5) Throttle	1/4 OPEN
6) Boost Pump	ON 4 SEC
7) Boost Pump	OFF
8) Clear Propeller	LOOK and call “CLEAR”
9) Starter	ENGAGE
10) On Start	1000 RPM
11) Oil Pressure	CHECK
(Shut down if inadequate)
12) Flaps	UP
13) Alternator	ON
14) Avionics Master	ON
15) Avionics	ON

COLD STARTING

Cold starts are similar, except more fuel may be required, implying longer boost pump operation. For temperatures below 20F, pre-heating is recommended.

FLOODED ENGINE - (Starting Checklist)
1) Mixture	CUT-OFF
2) Propeller	HIGH RPM
3) Throttle	1/2 OPEN
4) Crank engine
5) Upon start, throttle	IDLE
6) Mixture	RICH

WARNING
Should a backfire occur during any start, continue cranking to draw any fire back into the engine. If backfiring continues or fire starts, exit the airplane and use fire extinguisher to put out fire.

PRE-TAXI CHECKS - (Checklist)
1) Taxi Clearance	Obtain and read back
2) Clear aft area prior to power	Clear
3) Brakes	CHECK

PRE TAKE-OFF RUN-UP - (Checklist)
1) Door	LOCKED
2) Area	CLEAR
3) Brakes	SET
4) CHT/Oil Temp	GREEN
5) Throttle	1700 RPM
6) Propeller	CYCLE twice
7) Mags	CHECK for 50 RPM drop
8) Instrument Vacuum	CHECK 4.5-5.5 in. Hg.
9) Throttle	IDLE, 1000 RPM

BEFORE TAKE-OFF - (Checklist)
1) Door	LOCKED
2) Seat belts	SECURE
3) Instruments	CHECK
4) Fuel Quantity	CHECK
5) Oil Temp./Press	GREEN/CHECK
6) Breakers	IN
7) Master switch/Avionics master	ON
8) Radios	SET
9) Transponder	STANDBY
10) Propeller	IN
11) Mixture	FULL RICH
12) Boost Pump	ON
13) Trim	SET TAKE-OFF
14) Flaps	SET 15 DOWN
15) Controls	Check FREE
16) Cowl Flaps	Check OPEN

RUNWAY CHECKS (After Cleared) (Checklist)
1) Strobes	ON
2) Transponder	ON ALT
3) Approach and Take-off area	CLEAR
4) Clearance from Tower	RECEIVED
5) Runway and approach	CLEAR
6) Time	NOTE

TAKE-OFF AND CLIMB - (Checklist)
1) Take-off Power	2700 RPM
2) Oil Temp (Green)	120F minimum
3) Cylinder Head Temp (Green)	140F minimum
4) Check engine instruments
5) Check Flight Instruments
6) Rotate	65 kts (75 mph)
7) Initial climb	90 kts (104 mph)
8) At  700 feet AGL	FLAPS UP
9) Reduce power	25 in., 2500 RPM
10) Mixture	LEAN for Climb*
11) Cylinder Head Temp (Green)	430F Maximum12) 12) Oil Temp	240F Maximum
13) Boost Pump	Check Press., OFF

CRUISE - (Checklist)
1) Throttle	SET
2) Propeller	SET (Max 2500 RPM)
3) Mixture	LEAN*
4) Cowl Flaps	CLOSE
5) Fuel tanks	MONITOR

* LEANING RULES

A. Never exceed the maximum cylinder head temperatures

B. For maximum service life, CHT’s should be maintained below 435F (224C) during high performance cruise operations and below 400F (205C) for economy cruise powers.

C. Maintain “Full Rich” for Take-off, climb, and cruise power settings of above 75% power. For Take-Off from high altitude airports, if engine roughness is noted, lean only enough to obtain smooth operation. Be alert for temperature rise. This is most likely to occur at altitudes over 5000 feet, and may require opening of cowl flaps.

D. Always return to full rich before increasing power settings.

E. Operate the engine at maximum power mixture for performance cruise powers and at best economy mixture for economy cruise power.

F. During let-down flight operations it may be necessary to manually enrichen fuel/air mixture.

G. Changes to cruise altitude and/or power settings require the mixture to be reset.

LEANING, EXHAUST GAS TEMPERATURE

A. Maximum power cruise - (Approx 75% power) - 150F on rich side of peak EGT for best power. Monitor cylinder head temperature.

B. Best economy cruise - (Approx 75% power or below) - Operate at 50F lean of peak EGT.

LEANING, FLOWMETER

Lean to the applicable fuel-flow tables.

LEANING, MANUAL MIXTURE CONTROL

1) Slowly move mixture control from “Full Rich” towards lean position.
2) Continue leaninguntil slight loss of power or onset of roughness.
3) Enrich until roughness or loss of power cease.

ADDITIONAL CHECKLISTS

DESCENT - (Checklist)
1) Master Switch	ON
2) Mags	BOTH
3) Fuel Tank	FULLEST TANK
4) Fuel Boost Pump	ON within 1000 feet AGL
5) Altimeter	SET
6) Mixture	Enrichen thru descent to FULL RICH
7) Power	As required
8) CHT’s	Greater than 180F

PRE-LANDING - (Checklist)
1) Seat Belts	SECURE
2) Fuel Tank	Fullest
3) Mixture	RICH
4) Flaps	FULL
5) Propeller	IN
6) Brakes	CHECK
7) Establish	NORMAL APPROACH
8) Fuel Boost Pump	ON

BALKED LANDING - (Checklist)
1) Throttle	FULL
2) Airspeed	85 kts(98 mph)
3) Establish climb
4) Flaps	RETRACT

(After leaving runway)
1) Fuel boost pump	OFF
2) Flaps	UP
3) Strobes	OFF
4) Transponder	OFF
5) Lights	As required
6) Trim	Reset to Take-Off
7) Time	Note

SHUTDOWN - (Checklist)
1) Radios	OFF
2) Avionics Master	OFF
3) Throttle	1200 RPM
4) Mixture	IDLE CUT-OFF
5) Mags	OFF
6) Lights	OFF
7) Master Switch	OFF
8) Control Lock	INSTALLED
9) Chocks/Tiedown	SECURE
10) Brakes	CHECK

ABBREVIATED TAKE-OFF CHECKLIST (CIGAR)

Controls	FREE

Instruments
Breakers	IN
Altimeter	SET
Directional Gyro	SET
Radios	SET
Engine Instruments	GREEN

Gas
Boost Pump	ON
Fuel Pressure	OK
Fuel Tanks	FULL
Mixture	RICH

Attitude
Door	SECURE
Seat Belts	SECURE
Flaps	SET
Trim	SET

Run-up
Brakes	SET
Nose wheel	Straight
Mag check	1700 RPM, 150 max drop
Propeller	TWO CYCLES
Oil Pressure	GREEN

ABBREVIATED LANDING CHECK-LIST - (GUMP)

Gas
Tank	FULLEST
Boost Pump	ON
Fuel Pressure	GOOD

Under Carriage
Brakes	CHECK
Flaps	SET 1/3 at 100 kts
Flaps	FULL at 90 kts

Mixture
Mixture Control	RICH

Prop
Propeller Control	IN

Heating and Ventilation
Cooling Air
To avoid any possibility of ingesting exhaust as part of the cooling air, and to avoid the need for additional surface obstructions, the cooling air intakes are included in the upper cowling, and accept air in the front top area of the engine cooloing air intake area. This also provides cooling air flow whenever the engine is running. This air is available to a pair of adjustable jets in the instrument panel, and another pair in the rear of the cabin for the back passengers. By operating the two side controls under the panel, cool air can also be routed into the front foot area.

In case of fire, the cooling air may be turned off by pulling the Fire/Air cutoff knob under the center of the panel.

Heating
Cabin heat is generated by a heat muff surrounding the front exhaust crossover. From there it passes through the firewall via a rotary control valve, which can shut off the heat flow, route it to the floor vents, and route it to the defrost vents, which are located in the glare shield. A control mounted at the bottom of the instrument panel. In addition, two sidewall mounted controls select warm or cold air for the rear of the cabin. If warm air is selected for the rear, then the outside cold air intakes must be set to cut-off. As an additional feature, if the heat is shut off with the heat control valve, then cold air may be routed to the floor outlets by setting the rear air selectors to warm air.

COLD WEATHER OPERATIONS
Pre-flight inspection of the Express aircraft is particurly important in cold weather, given the particularly slick design and laminar flow airfoils. Be sure that there are no frost or ice deposits, and that all the control surfaces are free to move properly.

Very cold temperature require special attention to engine operations. The general recommendation is to pre-heat the engine below 20 Deg. F, and avoid flight engine startups below 10 Deg. F.

Warm up the engine with particular care and attention paid to oil temperature being in the green before take-off. Also, verify the responsiveness of the engine to throttle inputs.

Also, cycle the propeller and ensure it is responding properly.

Flight in icing conditions is prohibited.

Performance

Section V

Table of Contents

INTRODUCTION TO PERFORMANCE
ALTIMETER CORRECTIONS
AIRSPEED SYSTEM CALIBRATION
STALL SPEEDS
TAKEOFF DISTANCES
RATE OF CLIMB
CRUISE SPEEDS
OTHER CHARTS
Cruise speed data
International standard atmosphere
Temperture conversion
Engine chart
SUMMARY

Weight and Balance

Section VI

Table of Contents

GENERAL
LOADING CHECKS
CARGO
DEFINITIONS
WEIGHT AND BALANCE REPORT
WEIGHT AND BALANCE RECORD